New Jeep Renegade Technical Specifications (Petrol)

|  | 1.6 E-torQ | 1.4 MultiAir II Manual | 1.4 MultiAir II DDCT | 1.4 MultiAir II 4WD Automatic |
| --- | --- | --- | --- | --- |
|  | Engine |
| Configuration | 4 cylinders | 4 cylinders | 4 cylinders | 4 cylinders |
| Cubic capacity (cc) | 1598 | 1368 | 1368 | 1368 |
| Valves | 16 | 16 | 16 | 16 |
| Bore x stroke (mm) | 77x85.8 | 72x84 | 72x84 | 72x84 |
| Compression ratio | 11.0:1 | 9.8:1 | 9.8:1 | 9.8:1 |
| Fuel type | Unleaded | Unleaded | Unleaded | Unleaded |
| Fuel system | Coil-on-plug, spark plugs with dual precious metals |
| Max power – kw (hp) @ rpm | 81 (110) @ 5500 | 103 (140) @ 5500 | 103 (140) @ 5500 | 125 (170) @ 5500 |
| Max torque – Nm @ rpm | 152 @ 4500 | 230 @ 1750 | 230 @ 1750 | 250 @ 2500 |
|  | Transmission |
| Gearbox | 5 speed Manual | 6 speed manual | DDCT | 9 Speed Automatic |
|  | Suspension |
| Front | MacPherson independent wheels |
| Rear | MacPherson independent wheels |
|  | Steering |
| Type | Electric power steering |
| Overall ratio | 15:07 | 15:07 | 15:07 | 15:07 |
| Steering turns (lock to lock) | 2.68 | 2.68 | 2.68 | 2.68 |
| Turning circle (kerb to kerb in metres) | 11.07 | 11.07 | 11.07 | 11.07 |
|  | Brakes |
| Front | 305 x 28 | 281 x 26 | 281 x 26 | 305 x 28 |
| Rear | 278 x 12 | 278 x 12 | 278 x 12 | 278 x 12 |
|  | Dimensions |
| Height – Max (mm) | 1667 | 1667 | 1667 | 1684 |
| Length (mm) | 4236 | 4236 | 4236 | 4236 |
| Width (mm) | 1805 | 1805 | 1805 | 1805 |
| Wheelbase (mm) | 2570 | 2570 | 2570 | 2570 |
| Track front/rear (mm) | 1541 | 1541 | 1541 | 1541 |
|  | 4x4 Capability |
| System | Front-Wheel Drive | Front-Wheel Drive | Front-Wheel Drive | Four Wheel Drive |
| Running ground clearance – front/rear (mm) | 175 | 175 | 175 | 175 |
| Approach/Departure/Breakover angle (degrees) | 17.9 / 29.7 / 21.2 | 17.9 / 29.7 / 21.2 | 17.9 / 29.7 / 21.2 | 17.9 / 29.7 / 21.2 |
|  | Weights and Capacities |
| Kerb weight max (kg) | 1346 | 1356 | 1380 | 1472 |
| Gross vehicle weight (kg) | 1905 | 1865 | TBC | TBC |
| Max payload (kg) | TBC | 470 | TBC | TBC |
| Max towing weight – braked trailer (kg) | 1000 | 1000 | 1000 | 1000 |
| Max towing weight – unbraked trailer (kg) | TBC | 400 | TBC | TBC |
| Fuel tank capacity (l) | 48 | 48 | 48 | 48 |
| Max cargo volume – seats up [ISO 3832] | 351 | 351 | 351 | 351 |
| Max cargo volume – seats down [ISO 3832] | 1297 | 1297 | 1297 | 1297 |
|  | Performance |
| 0-100km/h (secs) | 11.8 | 10.9 | 11.0 | 8.8 |
| Max speed (mph) | 111 | 112 | 112 | 122 |
|  | Fuel Consumption |
| Combined cycle mpg (l/100km) | 6.0) | 47.1 (6.0) | 47.9 (5.9) | 40.9 (6.9) |
| Extra Urban cycle mpg (l/100km) | 56.5 (5.0) | 55.4 (5.1) | 56.5 (5.0) | 48.7 (5.8) |
| Urban cycle mpg (l/100km) | 36.2 (7.8) | 37.2 (7.6) | 37.7 (7.5) | 32.1 (8.8) |
|  | Emissions |
| EU emissions standard | Euro 6 | Euro 6 | Euro 6 | Euro 6 |
| CO2 (g/km) | 141 | 140 | 137 | 160 |
|  | Servicing |
| Service schedule (months/miles) | 12/9,000 | 12/9,000 | 12/9,000 | 12/9,000 |

New Jeep Renegade Technical Specifications (Diesel)

|  | 1.6 MultiJet II Diesel Manual | 2.0 MultiJet II Diesel 4WD Manual | 2.0 MultiJet II Diesel 4WD Automatic | 2.0 MultiJet II Diesel 4WD AutoTrailhawk |
| --- | --- | --- | --- | --- |
|  | Engine |
| Configuration | 4 cylinders | 4 cylinders | 4 cylinders | 4 cylinders |
| Cubic capacity (cc) | 1598 | 1956 | 1956 | 1956 |
| Valves | 16 | 16 | 16 | 16 |
| Bore x stroke (mm) | 79.5 x 80.5 | 83 x 90.4 | 83 x 90.4 | 83 x 90.4 |
| Compression ratio | 16.5:1 | 16.5:1 | 16.5:1 | 16.5:1 |
| Fuel type | Diesel | Diesel | Diesel | Diesel |
| Fuel system | Multi-Jet II common rail with electronic high-pressure injection |
| Max power – kw (bhp) @ rpm | 88.3 (120) @ 3750 | 103 (140) @ 3750 | 103 (140) @ 3750 | 125 (170) @ 3750 |
| Max torque – Nm @ rpm | 320 @ 1750 | 350 @ 1750 | 350 @ 1750 | 350 @ 1750 |
|  | Transmission |
| Gearbox | 6 speed Manual | 6 speed manual | 9 Speed Automatic | 9 Speed Automatic |
|  | Suspension |
| Front | MacPherson independent wheels |
| Rear | MacPherson independent wheels |
|  | Steering |
| Type | Electric power steering |
| Overall ratio | 15:07 | 15:07 | 15:07 | 15:07 |
| Steering turns (lock to lock) | 2.68 | 2.68 | 2.68 | 2.68 |
| Turning circle (kerb to kerb in metres) | 11.07 | 11.07 | 11.07 | 11.07 |
|  | Brakes |
| Front | 305 x 28 | 305 x 28 | 305 x 28 | 305 x 28 |
| Rear | 278 x 12 | 278 x 12 | 278 x 12 | 278 x 12 |
|  | Dimensions |
| Height – Max (mm) | 1667 | 1684 | 1684 | 1697 |
| Length (mm) | 4236 | 4236 | 4236 | 4236 |
| Width (mm) | 1805 | 1805 | 1805 | 1805 |
| Wheelbase (mm) | 2570 | 2570 | 2570 | 2570 |
| Track front/rear (mm) | 1541 | 1541 | 1541 | 1541 |
|  | 4x4 Capability |
| System | Front-Wheel Drive | Four Wheel Drive | Four Wheel Drive Low | Four Wheel Drive Low |
| Running ground clearance – front/rear (mm) | 175 | 198 | 198 | 210 |
| Approach/Departure/Breakover angle (degrees) | 17.9 / 29.7 / 21.2 | 21 / 32.1 / 23.5 | 21 / 32.1 / 23.5 | 30 / 34 / 24 |
|  | Weights and Capacities |
| Kerb weight max (kg) | 1404 | 1502 | 1548 | 1548 |
| Gross vehicle weight (kg) | 1905 | 2010 | 2080 | 2080 |
| Max payload (kg) | 440 | 505 | 475 | 470 |
| Max towing weight – braked trailer (kg) | 1000 | 1000 | 1000 | 1000 |
| Max towing weight – unbraked trailer (kg) | 400 | 400 | 400 | 400 |
| Fuel tank capacity (l) | 48 | 48 | 48 | 48 |
| Max cargo volume – seats up [ISO 3832] | 351 | 351 | 351 | 351 |
| Max cargo volume – seats down [ISO 3832] | 1297 | 1297 | 1297 | 1297 |
|  | Performance |
| 0-100km/h (secs) | 10.2 | 9.5 | 10.2 | 8.9 |
| Max speed (mph) | 111 | 113 | 113 | 122 |
|  | Fuel Consumption |
| Combined cycle mpg (l/100km) | 61.4 (4.6) | 55.4 (5.1) | 49.6 (5.7) | 48.7 (5.8) |
| Extra Urban cycle mpg (l/100km) | 70.6 (4.0) | 61.4 (4.6) | 55.4 (5.1) | 55.4 (5.1) |
| Urban cycle mpg (l/100km) | 51.4 (5.5) | 47.1 (6.0) | 42.2 (6.7) | 40.9 (6.9) |
|  | Emissions |
| EU emissions standard | Euro 5+ | Euro 6 | Euro 6 | Euro 6 |
| CO2 (g/km) | 120 | 134 | 150 | 151 |
|  | Servicing |
| Service schedule (months/miles) | 12/12,000 | 12/12,000 | 12/12,000 | 12/12,000 |